## Slide 1
Data Communication and Networks
Data Encoding and Communication Interface
Dr. Spoorthi P Shetty
Associate Professor
Department of MCA
NMAM Institute of Technology, Nitte (Deemed to be University)

## Slide 2
• Signals which are continuous varying based on time.
Signal Representation
• Text, integers
Reasons for Representation
Digital Signal
• each pulse is a signal element
• Digital data, analog signal - optical fiber, unguided media, propagate analog signal
• Example: Voice, video, voltage, pressure, etc
• discrete, discontinuous voltage pulses
      Analog Signal
• Analog data, digital signal – modern digital transmission
• Digital data, Digital signal – less complex, less expensive
• binary data encoded into signal elements.
• Analog data, analog signal - data in electrical form can be transmitted as signal
easily and cheaply.

## Slide 3
Signal Encoding Techniques

## Slide 4
Unipolar — All signal elements of same sign (Either + or -)
Data rate (R) - amount of data transfer during a specified time period over a network in bps.
Modulation rate - A measure of how many individual signal elements are transmitted per unit time.
Cost and complexity - higher signal rate to achieve high data rate increases cost.
Polar - one + voltage level, other - voltage level (different representation)
Clocking - to know begin & end of bit position. (Provide separate clock both sides or provide synchronization)
Mark and space - 1 and 0 respectively
Terminologies
Signal spectrum - transfer power high at center, low at edges. Good signal design should concentrate on the transmission in middle of bandwidth.
Signal to noise ratio – (increase in SNR, decrease in bit error rate)
Bandwidth – maximum amount of data transmitted over an internet connection in a given amount of time. (increase in bandwidth, increase data rate)

## Slide 5
1—Transition at the beginning of interval
• lack of synchronization capability - when long string of 0’s and 1’s in NRZ-L and
long string of 0’s in NRZI
Easiest way to transmit digital data to digital signal
Cons
0—No transition
• not often used for signal transmission
NRZ-L (Nonreturn to Zero-Level)
Pros
Digital data to Digital Signal-Nonreturn to Zero
• used for magnetic recording
NRZI (NonReturn to Zero Inverted)
• easy to engineer
0—high level
• More reliable to detect a transition in presence of noise using NRZI
• make good use of bandwidth
2 types
1—low level
• Presence of dc component

## Slide 6
• Solution for this problem is: insert additional bits (scramble data)
• not as efficient as NRZ, because receiver distinguishes between three levels: +A, -A, 0
• lack of synchronization when long runs of 0’s in Bipolar-AMI and 1’s in Pseudoternary
Use more than two levels
• easy error detection
• 0 – no line signal
Disadvantage :
• 1 – +/− level alternating for successive ones
Multilevel Binary
2. Pseudoternary
Advantage :
Address the deficiencies of NRZ
• no loss of sync if a long string of 1’s occur
in Bipolar-AMI and 0’s in Pseudoternary
• 0 – +/− level alternating for successive zeroes
• 1 – no line signal
1. Bipolar-AMI

## Slide 7
Manchester
1—low to high
0—high to low
• has transition in middle of each bit period
• Always has transition in middle of each bit period
Biphase
1—no transition at start of bit period
2 types
0—transition at start of bit period
2. Differential Manchester Encoding

## Slide 8
Biphase Pros and Cons
• has no dc component
Cons
• requires more bandwidth
• maximum modulation rate is twice NRZ
• has error detection
• at least one transition per bit time and possibly two
Pros
• synchronization on mid bit transition (self clocking)

## Slide 9
Encoding Schemes

## Slide 10
Modulation Rate

## Slide 11
Previous mark polarity | Encode
+ | 000+-0-+
- | 000-+0+-
1. B8ZS (Bipolar with 8-zero substitution)
V (Violation), is signal have same polarity as the previous non-zero voltage.
B (Bipolar) is signal have opposite polarity as the previous non-zero voltage.
This technique is similar to Bipolar AMI except when eight consecutive zero-level voltages are encountered, they are
replaced by the sequence, “000VB0VB”.
There are two common scrambling techniques:
Scrambling Techniques
To address this, a technique called scrambling is used. Scrambling helps maintain synchronization without increasing the number of transmitted bits, making it an efficient solution.
Biphase encoding requires higher bandwidth, whereas NRZ (Non-Return to Zero) encoding faces issues such as synchronization problems and the presence of a DC component.
In the case of Bipolar AMI (Alternate Mark Inversion), although it eliminates the DC component, long sequences of zeros can still lead to synchronization loss.

## Slide 12
Previous mark polarity | Encode
+ | 000+-0-+
- | 000-+0+-
V (Violation), is signal have same polarity as the previous non-zero voltage.
B (Bipolar) is signal have opposite polarity as the previous non-zero voltage.
This technique is similar to Bipolar AMI except when eight consecutive zero-level voltages are encountered, they
are replaced by the sequence, “000VB0VB”.
B8ZS (Bipolar with 8-zero substitution)

## Slide 13
HDB3 (High-density bipolar3-zero)
If the number of nonzero pulses after the last substitution is odd, the substitution pattern will be “000V”, this helps maintaining total number of nonzero pulses even.
If the number of nonzero pulses after the last substitution is even, the substitution pattern will be “B00V”. Hence even number of nonzero pulses is maintained again.
Four consecutive zero-level voltages are replaced with a sequence “000V” or “B00V”.

## Slide 14
B8ZS and HDB3

## Slide 15
It has frequency range of 300Hz to 3400Hz use modem (modulator-demodulator)
Three types of Modulator techniques
0/1 binary values represented by different carrier amplitudes
The main use is public telephone system
Disadv: 1. inefficient
Example: LED – one- Presence of light, other- absence
Digital Data, Analog Signal: Modulation Techniques
1—presence of carrier
0—absence of carrier
1. Amplitude shift keying (ASK)
2. up to 1200bps on voice grade lines

## Slide 16
2. Binary Frequency Shift Keying
Two binary values represented by two different frequencies (near carrier frequency)
Used for up to 1200bps on voice grade lines high frequency radio
Less susceptible to error than ASK
More bandwidth efficient
More prone to error
Most common form of FSK is binary FSK (BFSK)
Even higher frequency on LANs using coaxial cable

## Slide 17
Differential PSK
• 0 - signal with same phase as FSK
Binary PSK—two phases represent two binary digits
2
3
• phase shifted relative to previous transmission rather than some reference signal
• each signal element represents more than one bit
• 1 - signal with opposite phase to previous one
Phase of carrier signal
• To make efficient use of bandwidth, Uses phase shifts of u/2 (90°)
1
Quadrature PSK
Phase Shift Keying

## Slide 18
Representation of Modulation Techniques

## Slide 19
Thank You

## Slide 20
Data Communication and Networks
Data Encoding and Communication Interface
Dr. Spoorthi P Shetty
Associate Professor
Department of MCA
NMAM Institute of Technology, Nitte (Deemed to be University)

## Slide 21
Techniques used are:
• Pulse code modulation
Digitizing Analog Data
Digital data can be converted to digital signal using any techniques like NRZ, Biphase etc.
Analog Data, Digital Signal
Digitization is conversion of analog data into digital data
• Delta modulation
Analog data to digital signal conversion is done using a codec device.

## Slide 22
According to the Nyquist Theorem, the sampling rate must be at least twice the highest frequency of the analog signal.
The analog signal is measured (sampled) at regular intervals.
Pulse Code Modulation
Sampling

## Slide 23
Each sampled value is approximated to the nearest value within a finite range of levels.
This introduces quantization error.
Quantization
Encoding
Each quantized value is then converted into a binary number (sequence of 0s and 1s).
These binary codes form the PCM signal.

## Slide 24
PCM Example

## Slide 25
Limitation:
• Example: 16 levels ⇒ 4 bits per sample
• To improve quality-8-bit quantization can be used ⇒ 256 levels-Better approximation of original signal-but consumes more data rate.
PCM Example Explanation
• Companding (Compressing + Expanding)
Quantization Process: Each PAM (Pulse Amplitude Modulated) sample is quantized:
Solutions to this problem are:
• Samples taken at 2B samples/second
Sampling Rate: According to Nyquist Theorem:
• i.e., one sample every 1/(2B) seconds
• Quantized values are only approximations
• Exact recovery of original signal is not possible due to Quantization Error
Bandlimited Signal: The original analog signal is assumed to have a bandwidth of B Hz.
• Nonlinear Encoding
• More levels = better approximation of original signal

## Slide 26
• Equal spacing ⇒ equal error across all amplitudes
Solution:
Nonlinear Encoding
• Low amplitude signals suffer greater relative distortion
Problem with Uniform Quantization:
• Use Nonlinear Quantization: More levels for low amplitudes
Fewer levels for high amplitudes
• Results in better overall signal quality

## Slide 27
Applies uniform quantization but modifies signal range:
Alternative to nonlinear quantization
• Increases gain for weak signals
• Expansion (at receiver):
Companding
• Restores original signal range
• Compression (at sender):
• Decreases gain for strong signals

## Slide 28
• At each sampling instant:
6
• Compare analog input to previous staircase value
8
7
Receiver reconstructs staircase from the bit stream
• Generate 1 if input > staircase, else 0
• 1 → Step up
Steps:
Output is smoothed using a lowpass filter
• 0 → Step down
Delta Modulation
3

## Slide 29
• At each sampling instant:
2
6
Requires only 1 bit per sample
Tracks the change (derivative) in signal, not absolute amplitude
• Compare analog input to previous staircase value
8
7
Receiver reconstructs staircase from the bit stream
Approximates an analog signal using a staircase function
4
5
• Generate 1 if input > staircase, else 0
A simplified alternative to PCM
Steps:
Output is smoothed using a lowpass filter
• 0 → Step down
The staircase steps up or down by a fixed amount (Δ) at each sampling interval
Delta Modulation
1
3

## Slide 30
• Mismatch = Error detected
• Transmitter:
Types of Error
• Compare with received check bits
• Frame: A contiguous block of bits transmitted together.
Principle of Error Detection
• Bit Error Rate (BER), Pb: Probability that a single bit is received in error.
• Receiver:
Types of Error
• Data (k bits) + Check bits (n - k) → Transmit n-bit frame
• Extract data and check bits
• Recompute check bits from received data
Bit errors may lead to incorrect data interpretation.
Transmission errors can occur due to noise, interference, or attenuation.

## Slide 31
Error Detection Process

## Slide 32
Even Parity - Parity bit ensures even number of 1s in data
Odd Parity - Parity bit ensures odd number of 1s in data.
Goal: Ensure the total number of 1s is either even or odd.
Parity Bit: A single bit added to a block of data (e.g., a character) to help detect errors.
Parity Check

## Slide 33
• Simple and Effective in detecting single-bit errors
• Since odd parity, odd number of 1s required.
Advantages
Parity Check-Example for Odd Parity
• Character: G → Binary: 1110001 (7 bits) - total number of 1s in G are 4.
• If total 1s remain odd → No error detected, else error detected.
• Cannot detect even-numbered bit errors
Limitations
• Add a 1 as parity bit → 11110001 - Hence Transmitted byte: 11110001

## Slide 34
• Digital logic
• if no remainder, assume no error
• Transmits n bits which is exactly divisible by some number
• Receiver divides frame by that number
• Modulo-2 arithmetic
One of the most common and powerful error detection methods.
Cyclic Redundancy Check (CRC)
3 Types
• for block of k bits, transmitter generates an n-k bit frame check sequence (FCS)
• Polynomial
In Modulo-2 arithmetic and polynomial:

## Slide 35
CRC Example
• P=110101=x=6 bits.
• M=1010001101=10 bits
• Hence number of bits in FCS=y=x-1=5 bits. Append 5 zeros to M
Answer:
Now, let us divide Q by P and calculate the remainder by performing an XOR operation between bits.
Step 1
Step 2
• 101000110100000, which makes Q.
Given
.
Consider the message sender wants to send is 1010001101, and the generator pattern is 110101. Find the message transmitted by the sender. If the receiver receives the message, check if the receiver receives the correct message or not.

## Slide 36
Now, the remainder is then replaced with the appended number of 0 bits in Q.
The input stream will be changed to 1010001101 + 01110 (original input data stream + remainder) = 101000110101110.
Thus, this data is then transferred over the internet and is received by the receiver. In the next step, the receiver will check whether the received bits are correct or not using the same method which was used in Step 2.
CRC Step 3
In this step, now receiver will perform the following division to check whether the received data is correct or not.
CRC Step 4
After division if the remainder is zero, then there is no error during transmission. Else error occurred during transmission.

## Slide 37
Thank You

## Slide 38
CRC-Polynomial
Similar to modulo 2 arithmetic but representation using polynomial.
• M = 1010001101 = X9 + X7 + X3 + X2 + 1,
• Pattern P = 110101 = X5 + X4 + X2 + 1
• Example:

## Slide 39
Q= Appending 3 bits to end of M, Q= X6 + X5
Answer:
Polynomial
M=4 bits P=4 bits hence FCS=3 bits
Question: Message is x3 + x2 and pattern P= x3 + x + 1. Find FCS using polynomial method and also check whether there is any error during transmission (introduce error in 4th bit position).

## Slide 40
Relies on retransmission when errors are detected.
Widely used in:
• Data Link Layer: e.g., HDLC
Waste of bandwidth,
Error Detection in Protocols
• Transport Layer: e.g., TCP
Forward Error Correction
Instead need to correct errors on basis of bits received.

## Slide 41
Thank You