## Slide 1
Dr. Spoorthi P Shetty
Associate Professor
Department of MCA
NMAM Institute of Technology, Nitte (Deemed to be University)
Data Communication and Networks
Introduction

## Slide 2
• Expansion beyond voice/data to include image and video content.
• Growth in services and traffic capacity.
• Mobile Broadband Traffic is exploding due to business use of smartphones and tablets.
Traffic Growth
• Steady increase in both local (in-building) and long-distance communication traffic.
• High-speed networks at competitive pricing encourage more mobile applications.
Technological Advances
• Business Demand Drivers: Web services/Remote access/Online transactions/Social networking.
Trends in Data Communication and Networking for Today’s Enterprise
Development of New Services
• Users Expect: High-resolution video/High-quality audio/Fast access to cloud and web applications.

## Slide 3
High-Speed LAN Requirements
Data Communication and Networking for Today’s Enterprise
Impact of Digital Electronics
Corporate Wide Area Networking (WAN) Needs

## Slide 4
Convergence = Merging of telephony and information technologies.
Convergence in Data Communication
Definition
Unified platform for voice, data, and video services.
Enables seamless, integrated communication across systems.

## Slide 5
Three-Layer Model of Convergence
Application Layer (End-User Level): Combines communication & business applications (e.g., Voice calling, voicemail, email, instant messaging).
Infrastructure Layer (Network Backbone): Voice, video, and image now transmitted over traditional data networks.
Mobile convergence: smartphones receive video, text, and data over cellular networks. Support for public/private cloud integration.
Enterprise Services Layer (Network Management): Network viewed as a function-providing system. Services include: Design & support of convergence facilities, QoS management, Authentication & user access control, Capacity management for users, groups, apps.

## Slide 6
Receiver: Converts signals from the transmission system back into usable data. Example: Modem
.
Destination: Final endpoint that uses the received data. Example: computer, server, or any end-user device
Transmission system: Medium through which signals are sent can be a
simple link or a complex network. Examples: transmission lines, fiber optics, internet backbone.
.
Communications Model
Source: Generates the original data. Examples: telephone, personal computer
Transmitter: Converts data from the source into transmittable signals. Performs transformation & encoding.
Example: Modem converts digital data to analog for telephone lines.

## Slide 7
Signal Generation: Produces electromagnetic signals, must be suitable for transmission and interpretable by receiver.
.
Exchange Management: Rules for two-way communication, Includes connection setup, turn-taking, data format, and error handling.
Transmission System Utilization: Efficient use of shared transmission facilities, Multiplexing to share capacity.
5
.
Interfacing: Device must connect to transmission system, ensures compatibility and signal transmission readiness.
2
Communications Tasks
4
3
1
.
Synchronization: Receiver must recognize signal start, end, and timing - Essential for accurate data interpretation.

## Slide 8
Routing: Chooses path through the network, may involve dynamic path selection in large networks.
Flow Control: Prevents sender from overwhelming the receiver, manages data transfer rate between systems.
8
9
10
Error Detection and Correction: Ensures data integrity, detects and corrects distorted or lost data during transmission.
Communications Tasks
Recovery:
Deals with faults and interruptions, Allows resumption or rollback of communication session.
6
7
Addressing: Identifies intended recipient in multi-device networks, ensures correct delivery.

## Slide 9
13
12
Network Management: Configuration, monitoring, and fault handling, Includes planning for future capacity and upgrades.
Communications Tasks
11
Security: Ensures privacy and data integrity, Prevents unauthorized access and tampering.
Message Formatting: Agreement on data structure and representation (e.g., character encoding), Ensures both parties interpret data identically.

## Slide 10
Data Communications

## Slide 11
• Offer high bandwidth; switching systems are still evolving.
• Used for voice, data, image, and video.
Key Requirements
• Common in medium and large offices.
• Communications software
Wide Area Networks (WANs)
• Users demand seamless connectivity between systems.
• Cover large geographic areas.
Networks
• High demand for integration and transmission capacity.
Local Area Networks (LANs)
• Networks
• Computers are rapidly increasing in number, power, and application scope.
Fiber Optics
• Offices often require multiple interconnected LANs.
The Growing Need for Networks
• Multiple types exist despite standardization.

## Slide 12
WAN Technologies
ATM (Asynchronous Transfer Mode): Fixed-size cells vs. variable-size frames in Frame Relay. Minimal error control overhead. Supports 10s to 100s of Mbps, even Gbps. Allows dynamic virtual channels with varied data rates. Combines benefits of circuit and packet switching.
Circuit Switching: Dedicated path between stations. Example: Telephone network.
Frame Relay: Designed for low error, high-speed networks. Less overhead, supports up to 2 Mbps. Faster than traditional packet switching.
Packet Switching: Data sent as packets, stored and forwarded at each node. Ideal for computer-to-computer communication.

## Slide 13
Flow Control
• Owned and managed by the organization using it.
• Higher data transfer speeds.
• Wireless LANs: Use various wireless technologies.
Types of LANs
• Enable mobility, easy setup, and flexible configuration.
Local Area and Wireless Networks
• Smaller scope.
• Switched LANs: Typically switched Ethernet.
Used in both LAN and WAN environments.
• Offers high internal data rates.
• Fully user-owned and maintained.
• Interconnects devices within a limited geographic area (e.g., building/campus).
• Widely adopted in business and communication systems.
Wireless Networks
• ATM LANs and Fibre Channel.
Differences from WANs

## Slide 14
Originated from ARPANET (1969), funded by the U.S. DoD.
First operational packet-switching network.
The Evolution of the Internet
Developed into the global Internet, now spanning billions of users and millions of hosts.
Key contributors: Vint Cerf & Bob Kahn – developed TCP/IP protocols.

## Slide 15
Internet Architecture
Hosts: (PCs, servers, mobile devices) connected via LANs/WANs.
Customer Premises Equipment (CPE): Connects users to ISP POPs.
Internet formed by hierarchical overlapping networks.
IP Datagrams: Routed from source to destination across networks.
Routers: Connect multiple networks, directing packets based on IP addresses.

## Slide 16
Access, Peering & Example Configuration

## Slide 17
• Dial-up (56Kbps), DSL, Cable Modem, Fiber.
CPE and Local Loop
• Common user connections:
• ISP connects to Internet via high-speed SONET links.
• NAPs: Major interconnection hubs for ISPs (e.g., MAE West).
Example Configuration
Peering & Network Backbone
• ISPs provide: IP address, name resolution, network access.
• ISPs connect via POPs, NAPs, and NSPs.
Access Technologies & Connections
• NSPs: Provide backbone services and peering agreements.
• Residential user connects via DSL/Cable to ISP.
• Private networks can connect through ATM/WAN routers.
• Business LAN uses Ethernet, connects to Internet via firewall.
• CPE connects to the Local Loop (the “last mile” to ISP).
Access, Peering & Example Configuration

## Slide 18
Thank You